## Slide 1: 2nd assignment for EG-151 main section of the example program – prog5.asm
LDHX #TABLE ;Point the index register to the table
CLRA ;Initialise the accumulator to zero
NEXT_NUMBER
ADD 0,X ;Add the indexed number to the accumulator
AIX #01 ;Increment the HX index register
CPHX #END_TABLE ;Has the last number been added?
BNE NEXT_NUMBER ;If not, branch back for next number
STA PTFD ;Otherwise send the total to the LED bar
LOOP
BRA LOOP ;This line "traps" the microprocessor
TABLE
FCB 1,2,3,4,5,6 ;form constant bytes; The table of numbers
;are stored in ROM.
END_TABLE
FCB 0 ;This is a dummy value to end the table

## Slide 2: Your tasks for this program
Draw a flow chart of the provided programme
Replace the number table with your student number.
You are to use two buttons to select between two student numbers.
  Draw a new flowchart for the revised programme (hint: reuse the code from Exercise 1)
  Implement the revised programme.