## Slide 1: Programs in experiments
CLR COUNTER ;Initial value of variable COUNTER = 0
COUNT_LOOP
LDA COUNTER ;Load the current value of COUNTER
STA PTFD ;Send it to Port F data register
INC COUNTER ;Increment the variable COUNTER (mod 256)
JSR SHORT_DELAY ;A short delay to make counting visible
BRA COUNT_LOOP ;Repeat for ever

## Slide 2: Programs in experiments
CLR COUNTER ;Initial value of variable COUNTER = 0
COUNT_LOOP
LDA COUNTER ;Load the current value of COUNTER
STA PTFD ;Send it to Port F data register
LDA PTDD ;Load the accumulator from port D
AND #BIT2 ;Mask the desired bit of port D
BEQ DECREMENT ;If the designated bit is zero, branch
INC COUNTER ;Otherwise Increment the variable COUNTER
BRA END_LOOP ;Branch to the next part of the loop
DECREMENT
DEC COUNTER ;This is the destination if button pressed
END_LOOP ;Arrive here regardless of button pressed
JSR SHORT_DELAY ;A short delay to make counting visible
BRA COUNT_LOOP ;Repeat for ever

## Slide 3: 1st exercise
Draw a flow chart of the existing programme
Modify existing program to achieve:
  fast speed by pressing SW4, and slow speed by pressing SW3, intermediate speed if not pressing any of them.
  Plan your changes by modifying your flowchart before implementing your solution in code.
(hint: to use SW3, make BIT3 = %00001000, then initialise it by sending BIT3 to PTDPE)